## Slide 1
Project Sponsors:
Autonomous Water Taxi
By: AutoPirates
Date: 05th November 2015
Preliminary Design Review
Team B: Tushar, Shiyu, Bikramjot, Tae-Hyung, William

## Slide 2
Content
Project description
Use case/System graphical representation
System-level requirements
Functional architecture
Cyber-physical architecture
Subsystem descriptions
Current system status
Project management

## Slide 3
Project Description

## Slide 4
Project Description
Problem
Pittsburgh lacks a viable river transportation system
Many attractions are located along the river
Currently, only luxury cruise lines available
Solution
AutoPirates is an autonomous water taxi service
A pleasant way to commute to work
More efficient than automobiles in reaching riverfront locations

## Slide 5
Use Case

## Slide 6
Use Case: System Graphical Representation
James would like to spend a nice day with his family, beginning with some shopping at Walmart, followed by an exciting game at PNC Park, and finally a nice dinner at the Cheesecake Factory in Southside Works.

## Slide 7
Use Case: System Graphical Representation
Welcome James!
Your Location : Monongahela
Destination : Southside Works
Estimated Fare : $13
Book Now
Powered by AutoPirates
Where you want to go today?
James books the cab from AutoPirates iOS app.

## Slide 8
Use Case: System Graphical Representation
Boat arrives to pick James family

## Slide 9
Use Case: System Graphical Representation
James confirms the destination on Operator Control Unit (OCU)
OCU also shows the path to his destination

## Slide 10
Use Case: System Graphical Representation
Boat avoids obstacles in between the path

## Slide 11
Use Case: System Graphical Representation
The destination arrives

## Slide 12
Requirements

## Slide 13
System Requirements: Mandatory Functional
The system shall
MF1. Control throttling and steering of the boat.
MF2. Detect static obstacles in the river with minimum size of 2mtx2mtx2mt with more than 85% accuracy.
MF3. Detect shores with more than 85% accuracy.
MF4. Autonomously navigate from source to destination at the maximum distance of 2 miles in not more than 15 minutes.
MF5. Avoid detected static obstacles with an accuracy of more than 95%.
MF6. Update the path within 5 sec after detecting new static obstacles.
MF7. Record sensor data up to duration of 15 minutes.
MF8. Replay saved sensor data.
MF9. Have a 2D simulator to test path planning algorithm.

## Slide 14
System Requirements
Desirable functional requirements
The system shall -
DF1. Track dynamic obstacles with minimum size of 1m x 1m x 1m.
DF2. Update the path within 2sec after detecting new dynamic obstacles.
Mandatory non-functional requirements
The system shall -
MNF1. Be tested in 25-30 field trials.
MNF2. Arrive within a radius of 15 meters of the desired destination.
MNF3. Be demonstrated in a video.
MNF4. Sail at a velocity not more than 15 mph.
Desirable non-functional requirements
The system shall -
DNF1. Obey the “rules of the road”.
DNF2. Estimate the shape of the static obstacles in the river with a minimum of 50% overlap.

## Slide 15
Architectures

## Slide 16
Functional Architecture: Defining functions of the project
Acquire data from Sensors
Filter data
Detect Dynamic Obstacles*
Detect Static Obstacles
Estimate path of obstacle*
Radar
User Input
Get destination
Get current location and localize
IMU/GPS
Plan route from current location to destination
Send commands to controller
Destination reached?
No
Yes
Destination
Log Data
Log Data
Perception
OCU
Planning
Log Playback
*Not in planned scope
Autonomously sail to destination

## Slide 17
Functional Architecture: Functioning with logged data and simulator
Acquire data
Filter data
Detect Static Obstacles
Logged Radar Data
Input (Config params)
Get destination
Get current location and localize
Logged IMU/GPS
Plan route from current location to destination
Destination reached?
No
Yes
Destination
Perception
User Input
Planning
Log Playback
Autonomously sail to destination in simulator

## Slide 18
Da
Da
Da
Da
Cyberphysical Architecture
Radar (Simrad 4G FMCW)
GPS/IMU Input and Output
IMU/GPS (Novotel Span)
Low Level Controller
(ARM based proprietary FPGA board of NREC)
Control Throttle and steering
Da
Perception Algorithm
Software System (Laptop)
Path Planning Algorithm
Raw Radar Data
Send GPS waypoints to control boat (ROS Topic)
Data Acquisition System
Obstacles Data
Da
Destination Input from User on GUI
OCU (Laptop)
Display Map and current Location
Engine (Twin 150 HP Engine) and Steering
Engine and steering controller
Engine and Steering Controller (Inbuilt)
SeaHawk OS 2700S
Development using ROS in C++
LAN
LAN
Same or different Laptop or Tablet as in software system
Publish IMU/GPS data as ROS TOPIC
Single Board Computer
(SBC running Linux and connected to LAN (Based on ROS))
Send Commands to control boat

## Slide 19
Subsystems

## Slide 20
Subsystem: Perception
Interface with ROS
Radar Data
Log Data
Data Filtering
Ego motion compensation
Morphological operation (open/close)
Contour Extraction
Object Detection (Boundary box)
Path Planning Algorithm
Obstacle Data Object
Acquire data using OpenCPN

## Slide 21
Subsystem: Path Planning
Get current location
IMU/GPS
Data from ROS Topic (SBC)
Log Data
Add obstacles to Occupancy Grid Map
Filter and localize
Path Planner
Obstacles data from perception algorithms
Get GPS waypoints of next grid location
Send GPS waypoints to SBC
Single Board Computer (SBC)
Create Occupancy Grid Map of environment
Operator Control Interface (OCU)

## Slide 22
Subsystem: Simulator
Get current location
Recorded data (ROS Topic)
Add obstacles to Occupancy Grid Map
Localize
Path Planner
Sample obstacle data for testing
Create Occupancy Grid Map of environment
Visualization of path

## Slide 23
Current Status

## Slide 24
Current Status: Perception
Integrated Radar with OpenCPN library

## Slide 25
Current Status: Perception
Integrated Radar to receive RAW data and visualized the data using ROS Node
Working to filter raw data collected from Radar

## Slide 26
Current Status: Perception
Noisy Image -> Morphological Operations -> Contour Extraction -> Object Detection

## Slide 27
Current Status: Path Planning
IMU/GPS Interfacing (Subscribed to ROS topic)
Functionality to log IMU Data

## Slide 28
Current Status: Path Planning
Implemented A* code in C++ using library having high performance
Built samples from SBPL libraries with different environment configurations and planners
Working on creating occupancy grid map of the location of river where we would be having test runs

## Slide 29
Current Status: Path Planning
Extracted data from OpenStreet Map in .osm format

## Slide 30
Project Management

## Slide 31
Fall Validation Experiments: Perception
Step ID | Step Description | Success Condition | Conditions
PE.1 | Start RGB video of field test | This is our ground truth | Location: NSH Demonstration on laptop (Simulation), Projector required
PE.2 | Simultaneously replay and visualize saved raw radar data in ROS | We can see plots of the radar image | 
PE.3 | Show filtered data | The filtered image has less noise than the raw image | 
PE.4 | Demonstrate obstacle detection | Draw bounding box around the obstacles. | 
PE.5 | Show detected objects from radar image while showing recorded video | The radar should detect obstacles that are in the video, at least the boats | 

## Slide 32
Fall Validation Experiments: Path Planning and Simulator
Step ID | Step Description | Success Condition | Conditions
PL.1 | Interfacing with IMU/GPS | Display logged data from IMU/GPS which we would be collecting during a field test | Location: NSH Demonstration on laptop (Simulation), Projector required
PL.2 | Generate Environment Map | Display occupancy grid map for 2 miles with filled blocks depicting obstacles (For one of the rivers of Pittsburgh) | 
PL.3 | Demonstrate Path Planning | Boat successfully navigates from Point A to Point B in simulator which are 1 mile apart | 
PL.4 | Show obstacle avoidance | Boat successfully avoids obstacles in simulator in the above task. Obstacles are static and are simulated through occupancy grip map | 

## Slide 33
Spring Validation Experiments: Script for final demo
Step ID | Step Description | Success Criteria | Conditions
SV.1 | Get the boat on the river | Location: center of width | Location: Allegheny River (Exact location is yet to be provided by the sponsor) Equipment /Arrangements: Boat, Radar, IMU/GPS, Fuel, Laptop in boat, Camera to record video, safety driver
SV.2 | Keep 5 static obstacles in the path | Size more than 2mx2mx2m | 
SV.3 | Switch on the engines and start AutoPirates autonomous system | The system starts successfully | 
SV.4 | Enter the destination through OCU | OCU takes the location correctly | 
SV.5 | The boat navigates autonomously and avoids obstacles | Boat avoids at least 4 obstacles | 
SV.6 | The boat arrives the destination | Boat arrives to destination (15 mts radius) | 
SV.7 | Show logged file | Play back logged data | 
SV.8 | Turn off the autonomous system and engine | System switches off without any error | 

## Slide 34
Budget Allocation
Hardware/Equipment/Budget provided by the sponsor (NREC) |  |  | 
S.No | Part | Part Name | Quantity
1 | Boat | 2015 SeaHawk OS 2700S | 1
2 | Radar | SimRad 4G FMCW Radar | 1
3 | Lidar | Velodyne VLP-16 | 1
4 | IMU/GPS | Novatel SPAN with IMU positioning | 1
5 | Laptop | Dell i7 | 5
6 | Proprietary Boards | SBC and Microcontroller boards | 2
7 | Trails for testing | $800 per trial | 25 (trails)
From RI Budget $4000 |  |  |  |  | 
S.No | Name | Description | Quantity | Cost | Total
1 | Transportation | Travel to NREC (5 people) | 64 | 25 | 1600
2 | Videography | Professional video of the final run | 1 | 500 | 500
3 | Backup for Trails | Incase we run out of allotted 25 trails | 2 | 800 | 1600
4 | Miscellaneous | To buy camera, contraption, books, etc | 1 | 300 | 300

## Slide 35
Work Breakdown Structure
Autonomous Water Taxi
Get data from Radar
Perception
Filter data
Morphological operation
Import external navigation map
Mapping & Localization
Generate occupancy grid map
Localize boat on the map
Generate a world model
Simulator
Generate a boat model
Apply path planning algorithm to the boat model
Integration
Integrate SBPL library with external map
Integrate perception with path planning
Input destination and waypoints
OCU
show obstacles
show real-time location
Sensor test
Testing
Algorithms test
Field test
Task scheduling
Project Management
Field management
Budget management
Contour extraction
Obstacle detection
Interface IMU/GPS
Path planning
Position and pose estimation
Interface SBPL library
Algorithm evaluation
Send command to low-level controller
Overlay radar image on the map
Evaluate performance for obstacles avoidance
show estimate path
Performance evaluation
Risk management
Integrate OpenCPN with ROS

## Slide 36
Schedule: 1

## Slide 37
Schedule: 2

## Slide 38
Risk Assessment
Risk ID | Risk Title | Req | Type | Description | Impact Statement | Likeli- hood (1-5) | Conse- quences(1-5) | Mitigating Actions
1 | Test environment availability | All | Testing | Won’t be able to do field testing because of weather conditions | Delay in the progress and insufficient data collect for algorithms | 4 | 3 | Test radar perception on shore for static obstacles. Use a simulator for path planning
2 | Limited testing trials | MNFR2 | Project management | Only 25-30 field tests | Unable to do system integration before demonstration | 5 | 3 | Appoint a field manager to plan logistics of each test.
3 | Radar Performance | MF2, MF3, DF1, DF2 | Technical | Radar signal is too noisy | Inadequate object detection with only radar | 3 | 4 | Incorporate additional sensors like Lidar and camera
4 | Localization accuracy | MF4, MF5 | Technical | Path planning algorithm relies on precise localization. GPS performance might be not as good as expected. | Poor estimation of the environment and poor navigation performance. | 3 | 5 | filter GPS data; limit the maximum speed of the boat

## Slide 39
Risk Assessment
Risk ID | Risk Title | Req | Type | Description | Impact Statement | Likeli- Hood (1-5) | Conse- Quences (1-5) | Mitigating Actions
5 | Insufficient boat protection | All | Testing | No automatic stop in case of a possible collision | The boat will collide with obstacles | 2 | 5 | Develop fail-safe software module
6 | Technical support from NREC | All | Technical | Limited availability from NREC engineers | It takes time for NREC engineers to fix hardware problems or to provide guidance for software | 4 | 3 | Ask for software documentations
7 | Team Communication | All | Project management | Language barrier in the team | It may be difficult to express ideas. | 4 | 2 | Do more preparations before the meetings

## Slide 40
Risk Assessment

## Slide 41
Questions