## Slide 1
Project Sponsors:
Autonomous Water Taxi
By: AutoPirates
Date: 29 Feb 2016
Critical Design Review
Team B: Tushar, Shiyu, Bikramjot, Tae-Hyung, William

## Slide 2
Content
Project description
Use case/System graphical representation
System-level requirements
Current system status
Project management
Conclusions

## Slide 3
Project Description

## Slide 4
Project Description
Problem
Pittsburgh lacks a viable river transportation system
Many attractions are located along the river
Currently, only luxury cruise lines available
Solution
AutoPirates is an autonomous water taxi service
A pleasant way to commute to work
More efficient than automobiles in reaching riverfront locations

## Slide 5
Use Case

## Slide 6
Use Case: System Graphical Representation
James would like to spend a nice day with his family, beginning with some shopping at Walmart, followed by an exciting game at PNC Park, and finally a nice dinner at the Cheesecake Factory in Southside Works.

## Slide 7
Use Case: System Graphical Representation
Welcome James!
Your Location : Monongahela
Destination : Southside Works
Estimated Fare : $13
Book Now
Powered by AutoPirates
Where you want to go today?
James books the cab from AutoPirates iOS app.
*Phone App not in scope

## Slide 8
Use Case: System Graphical Representation
Boat arrives to pick James family

## Slide 9
Use Case: Reality check
James confirms the destination on Operator Control Unit (OCU)
OCU also shows the path to his destination

## Slide 10
Use Case: System Graphical Representation
Boat avoids obstacles and pylons in between the path.
It also navigates successfully under the bridges.

## Slide 11
Use Case: System Graphical Representation
The destination arrives

## Slide 12
Requirements

## Slide 13
System Requirements: Mandatory Functional
The system shall
MF1. Interfacing with low level controller on boat, IMU/GPS and Radar
MF2. Detect static obstacles in the river with minimum size of 2mtx2mtx2mt with more than 85% accuracy.
MF3. Segment shores and bridges
MF4. Autonomously navigate from source to destination at the maximum distance of 2 miles in not more than 15 minutes.
MF5. Avoid detected static obstacles with an accuracy of more than 95%.
MF6. Update the path within 5 sec after detecting new static obstacles.
MF7. Record sensor data up to duration of 15 minutes.
MF8. Replay saved sensor data.
MF9. Have a 2D simulator to test path planning algorithm.
MF.10 Generate Occupancy grid map of environment
Not Tested
Tested during field tests
Partially Tested (Re-planning)

## Slide 14
System Requirements
Desirable functional requirements
The system shall -
DF1. Track dynamic obstacles with minimum size of 1m x 1m x 1m.
DF2. Update the path within 2sec after detecting new dynamic obstacles.
Mandatory non-functional requirements
The system shall -
MNF1. Be tested in 25-30 field trials.
MNF2. Arrive within a radius of 15 meters of the desired destination.
MNF3. Be demonstrated in a video.
MNF4. Sail at a velocity not more than 15 mph.
Desirable non-functional requirements
The system shall -
DNF1. Obey the “rules of the road”.
DNF2. Estimate the shape of the static obstacles in the river with a minimum of 50% overlap.
Out of scope
Done/Adhering
Working on it

## Slide 15
Current Status

## Slide 16
Current Status: Perception | Fall’15

## Slide 17
Current Status: Perception | Fall’15 Video

## Slide 18
Current Status: Perception | Filtering Improvements in Spring
Octomap: Radar data converted to Octomap
Less noise as compared to binomial filtering

## Slide 19
Current Status: Path Planning | Field Test 3 | One Time Planning

## Slide 20
Current Status: Path Planning | Field Test 3 | Continuous Re-planning (partially successful)

## Slide 21
Current Status: Simulator
Fake Obstacles
Static
Random Dynamic
Tele-operated

## Slide 22
Current Status: Integration (To be tested during Field Test 4)

## Slide 23
Project Management

## Slide 24
Work Breakdown Structure | Schedule Status
Autonomous Water Taxi
Get raw data from Radar
Perception
Filter data
Morphological operation
Import external navigation map
Mapping & Localization
Generate occupancy grid map
Localize boat on the map
Generate a world model
Simulator
Apply path planning algorithm to the boat model
Integration
Integrate SBPL library with external map
Integrate perception with path planning
Sensor test
Testing
Algorithms test
Field test
Task scheduling
Project Management
Field management
Budget management
Contour extraction
Obstacle detection
Interface IMU/GPS
Path planning
Position and pose estimation
Interface SBPL library
Algorithm evaluation
Send command to low-level controller
Overlay radar image on the map
Evaluate performance for obstacles avoidance
Performance evaluation
Risk management
Integrate OpenCPN with ROS
Optimize radar filters
Dynamically run planner
Finished
Subsystem
In progress
Not started

## Slide 25
Spring Validation Experiments: Test Plan
PR No. | Date | Milestones
PR.7 | Jan 27 | Improve costmap functionality and path planning simulation
PR.8 | Feb 10 | Robust single time planning and re-planning (in progress)
PR.9 | Feb 24 | Improve Filtering of Radar data
PR.10 | Mar 16 | Integrate radar obstacles with path planner and re-planning
PR.11 | Mar 30 | Rules of road and dry run to Identify and practice exact scenario for SVE
PR.12 | Apr 11 | Back up to fix bugs or enhace performance
Field Test 3
Field Test 4
Field Test 5
Field Test 6

## Slide 26
Spring Validation Experiments: Script for final demo

## Slide 27
Budget Allocation
Hardware/Equipment/Budget provided by the sponsor (NREC) |  |  | 
S.No | Part | Part Name | Quantity
1 | Boat | 2015 SeaHawk OS 2700S | 1
2 | Radar | SimRad 4G FMCW Radar | 1
3 | Lidar | Velodyne VLP-16 | 1
4 | IMU/GPS | Novatel SPAN with IMU positioning | 1
5 | Laptop | Dell i7 | 5
6 | Proprietary Boards | SBC and Microcontroller boards | 2
7 | Trails for testing | $800 per field test | 25
From RI Budget $4000 |  |  |  |  |  |  | 
S.No | Name | Description | Quantity | Cost | Total | Spent | Left
1 | Transportation | Travel to NREC (5 people) | 64 | 25 | 1600 | 50 | 1550
2 | Videography | Professional video for NREC | 1 | 500 | 500 | 0 | 500
3 | Backup for Trails | Incase we run out of allotted 25 trails | 2 | 800 | 1600 | 0 | 1600
4 | Miscellaneous | To buy camera, contraption, books, etc | 1 | 300 | 300 | 54 | 246
3896
Available

## Slide 28
Risk Assessment
Risk ID | Risk Title | Req | Type | Description | Impact Statement | Likeli- hood (1-5) | Conse- quences(1-5) | Mitigating Actions
1 | Test environment availability | All | Testing | Won’t be able to do field testing because of weather conditions | Delay in the progress and insufficient data collect for algorithms | 4 | 3 | Test radar perception on shore for static obstacles. Use a simulator for path planning
2 | Limited testing trials | MNFR2 | Project management | Only 25-30 field tests | Unable to do system integration before demonstration | 5 | 3 | Appoint a field manager to plan logistics of each test.
3 | Radar Performance | MF2, MF3, DF1, DF2 | Technical | Radar signal is too noisy | Inadequate object detection with only radar | 3 | 4 | Incorporate additional sensors like Lidar and camera

## Slide 29
Risk Assessment
Risk ID | Risk Title | Req | Type | Description | Impact Statement | Likeli- Hood (1-5) | Conse- Quences (1-5) | Mitigating Actions
4 | Radar cannot detect bridge supports | All | Technical | The Radar only has 2D information | We can’t plan path without knowing the location of the bridge supports | 5 | 5 | Research nautical maps that has information for the bridge supports
5 | Code Efficiency | All | Technical | Code may run too slow after integration | Poor system performance | 5 | 4 | Integration early and often to identify bottlenecks
6 | Team Communication | All | Project management | Language barrier in the team | It may be difficult to express ideas. | 4 | 2 | Do more preparations before the meetings

## Slide 30
Risk Assessment

## Slide 31
Questions